## Slide 1
Fall 2021 OpenAirInterface Workshop: Lab3 - Network slicing with OAI 5G CN
Tien Thinh NGUYEN
Notes: <number>

## Slide 2
Network Slicing - Overview
<number>
Fall 2021 OAI Workshop: Lab3
Overview of Network Slicing
  As a crucial enabler to realize the service-oriented 5G vision
  Allow multiple logical networks to be created on top of a common shared physical infrastructure
  Multiple Network Slice instances delivering the same features but for different group of UEs/Services
A Network Slice is identified by an S-NSSAI with:
    A Slice/Service Type (SST): refers to the expected Network Slice behavior in terms of features and services. Some standardized SST values: eMMB, URLLC, MIoT, V2X
    A Slice Differentiator (SD): Differentiate amongst multiple Network Slices of the same SST
Notes: <number>

## Slide 3
Network Slicing with OAI 5G CN (1)
<number>
Fall 2021 OAI Workshop: Lab3
Network slicing with OAI 5G CN
  With NSSF: Discover and select an appropriate AMF to support the requested slice (AMF re-allocation procedure (available Q1 2022))
  With NRF: Discover and select SMF/UPF for the requested slice (for a particular PDU session)
  Per UE and per PDU session
Notes: <number>

## Slide 4
Network Slicing with OAI 5G CN (2)
<number>
Fall 2021 OAI Workshop: Lab3
Preparation and Instantiation
  NFs are configured to support a set of Network slices (SST, SD) in the configuration/yaml file
  (automatic via a management and orchestration tool e.g., OSM, Trirematics (Mosaic5G project))
Network slice selection
  Discover and select an appropriate AMF to support the requested slice (with NSSF and AMF re-allocation feature (available Q1 2022))
  Discover and select SMF/UPF for the requested slice (for a particular PDU session)
RAN
AMF1
AMF2
NSSF
SMF1
SMF2
NRF
UPF1
UPF2
DN
UE
Notes: <number>

## Slide 5
Lab 3: Network slicing with OAI 5G CN (1)
<number>
Fall 2021 OAI Workshop: Lab3
Lab environment
  With basic deployment: AMF, SMF, UPF, NRF, UDM, AUSF, UDR
  With gNBSim (gNB/UE)
  2 Network Slices
    Common NFs: AMF, NRF, UDM, AUSF, UDR,
    Slice 1 (SST=128, SD=128): UE1 (session 1), gNB1, SMF1, UPF1 (SPGWU)
    Slice 2 (SST=129, SD=129): UE2 (session 1), gNB2, SMF2, UPF2 (VPP-UPF)
Notes: <number>

## Slide 6
Lab 3: Network slicing with OAI 5G CN (2)
<number>
Lab description
  Deploy 5G CN with predefined scenario (with yaml file for 5G CN)
  Deploy two gNBs with gNBSim (with yaml files for gNBSim)
  Verify the logs
  Ping from UEs/DNs to the DNs/UEs to verify the data path
  Capture the packets with
    Tshark: sudo tshark -i any 'net 192.168.11.0/24 or net 192.168.41.0/24 or icmp or sctp and not arp and not tcp’
    Tcpdump (Please don’t do it now!)
sudo tcpdump -i any '(net 192.168.11.0/24 or net 192.168.41.0/24 or net 192.168.71.0/24 or net 12.1.1.0/24)' -vv -X -w lab3.pcapng
      Filter with Wireshark: http or sctp or pfcp or icmp
Fall 2021 OAI Workshop: Lab3
Notes: <number>