## Slide 1: OpenAirInterface RAN Roadmap
Florian Kaltenberger (Eurecom, OSA)
OAI Fall Workshop, 8.12.2021

## Slide 2: OAI Projects

## Slide 3: 5G RAN Project Group
https://openairinterface.org/oai-5g-ran-project/
Sponsors Contributors

## Slide 4: OAI 5G deployment options
EPC
S1-MME
S1-U
X2-C
RAN
eNB
gNB-DU
gNB-DU
gNB-CU
gNB
F1
F1
AMF/UPF
NG-C/U
RAN
gNB-DU
gNB-DU
gNB-CU
gNB
F1
F1
Non-standalone (ENDC)
Standalone
Phase 1: “noS1” with OAI UE
Phase 2: EN-DC with COTS UE
Phase 3: SA with COTS UE
S1-U
Phase 4: SA with OAI UE
OAI UE
OAI UE

## Slide 5: OAI gNB features
Subcarrier spacings: 30kHz (FR1), 120kHz (FR2)
Bandwidth: 20/40/50/60/80/100 MHz (FR1), 50MHz (FR2)
Duplexing: static TDD, dynamic TDD, FDD
PHY channels: NR-PSS/NR-SSS, NR-PBCH, NR-PDCCH, NR-PDSCH, NR-CSIRS, NR-PUSCH, NR-PUSCH, NR-PRACH, NR-SRS
SISO & MIMO 2x2
MAC: SIB1, Contention free/Contention based RA procedure, dynamic UL/DL scheduler with HARQ procedures, MCS adaptation from HARQ BLER, CSI-RS, CSI measurement report handling, SR handling
RLC: AM/TM/UM
PDPC: Integrity protection and ciphering procedures
RRC: procedures for SA and NSA
Full list here: https://gitlab.eurecom.fr/oai/openairinterface5g/-/blob/develop/doc/FEATURE_SET.md

## Slide 6: Status of 5G NSA development
No split bearer, traffic is redirected to 5G cell
Current performance
  80Mbps DL throughput (with 64QAM)
  7Mbps UL throughput (with QPSK)
  Up to 2 users tested
Tested Core networks
  OAI EPC
  Nokia LTEbox
Tested UEs:
  Oppo Reno 5G
  Samsung A90 5G
  Samsung A42 5G
  Google Pixel 5G

## Slide 7: FR2 NSA status
Basic development of PHY & MAC for FR2 done
  120kHz subcarrier spacing
  Beamforming support (using GPIO to control external RF)
  Transmission of multiple SSBs
  Support for multiple PRACH occasions for initial beam correspondence.
Tests with OAI gNB + OAI UE ok
  Using intermediate frequency ~5GHz
  Real-time operation ok
  Initial beam selection ok
Interoperability with COTS phone: not yet
  Phone not even seeing 5G cell during inter-RAT measurements

## Slide 8: Status of 5G SA development
Current performance with COTS UE
  Latency: 9ms (mean)
  Stability: up to 1h (without pushing traffic too much)
  80Mbps max DL throughput
  7Mbps max UL throughput
Validated Core networks
  OAI 5GC and
  Nokia Sabox
  Free CN
Tested UEs
  Simcom SIMCOM8200EA
  Quectel RM500Q-GL
  Huawei Mate 30 pro (limited)
  OAI UE

## Slide 9
gNB ↔ CN5G
gNB
CN5G

## Slide 10
COTS UE
(Quectel)
60MHz (162PRBs), 30kHz SCS, 6DL/1S/2UL slots, SISO

## Slide 11: SA UE
Supporting "noS1" mode (DL and UL):
  Creates TUN interface to PDCP to inject and receive user-place traffic
  No connection to the core network
Supporting Standalone (SA) mode:
  UE can register with the 5G Core Network, establish a PDU Session and exchange user-plane traffic
Testing with rfsimulator and USRP
  Throughput currently limited but will be improved
Notes: OpenAirInterface 5G-NR UE Feature Set
Supporting "noS1" mode (DL and UL):
  Creates TUN interface to PDCP to inject and receive user-place traffic
  No connection to the core network
Supporting Standalone (SA) mode:
  UE can register with the 5G Core Network, establish a PDU Session and exchange user-plane traffic
NR UE PHY Layer
Initial synchronization
Time tracking based on PBCH DMRS
Frequency offset estimation
30KHz SCS for FR1 and 120 KHz SCS for FR2
Reception of NR-PSS/NR-SSS
NR-PBCH supports multiple SSBs and flexible periodicity
Reception of NR-PDCCH (including reception of DCI, polar decoding, de-scrambling, de-modulation, RB de-mapping, etc)
  common search space configured by MIB
  user-specific search space configured by RRC
  DCI formats: 00, 10, 01 and 11
Reception of NR-PDSCH (including Segmentation, LDPC decoding, rate de-matching, de-scrambling, de-modulation, RB de-mapping, etc).
  PDSCH mapping type A and B
  DMRS configuration type 1 and 2
  Single and multiple DMRS symbols
  PTRS support
  Support for 1, 2 and 4 RX antennas
  Support for up to 2 layers (currently limited to DMRS configuration type 2)
NR-PUSCH (including Segmentation, LDPC encoding, rate matching, scrambling, modulation, RB mapping, etc).
  PUSCH mapping type A and B
  DMRS configuration type 1 and 2
  Single and multiple DMRS symbols
  PTRS support
  Support for 1 TX antenna
  Support for 1 layer
NR-PUCCH
  Format 0 (2 bits for ACK/NACK and SR)
  Format 2 (up to 64 bits, mainly for CSI feedback)
  Format 1, 3 and 4 present but old code never dested (need restructuring before verification)
NR-PRACH
  Formats 0,1,2,3, A1-A3, B1-B3
NR-SRS
  Old code never dested (need restructuring before verification)
SS-RSRP
  RSRP measured on synchronization SSB (ok only for single SSB)
Highly efficient 3GPP compliant LDPC encoder and decoder (BG1 and BG2 are supported)
Highly efficient 3GPP compliant polar encoder and decoder
Encoder and decoder for short block
NR UE FAPI
MAC -> PHY configuration via UE FAPI P5 interface
Basic MAC to control PHY via UE FAPI P7 interface
PHY -> MAC indication (needs some improvement)
NR UE Higher Layers
UE MAC
Minimum system information (MSI)
  MIB processing
  Scheduling of system information block 1 (SIB1) reception
Random access procedure (needs improvement, there is still not a clear separation between MAC and PHY)
  Mapping SSBs to multiple ROs
  Scheduling of PRACH
  Processing of RAR
  Transmission and re-transmission of Msg3
  Msg4 and contention resolution
DCI processing
  format 10 (RA-RNTI, C-RNTI, SI-RNTI, TC-RNTI)
  format 00 (C-RNTI, TC-RNTI)
  format 11 (C-RNTI)
  format 01 (C-RNTI)
UCI processing
  ACK/NACK processing
  Triggering periodic SR
  CSI measurement reporting (SSB RSRP only)
DLSH scheduler
  Configuration of fapi PDU according to DCI
  HARQ procedures
ULSCH scheduler
  Configuration of fapi PDU according to DCI
UE RLC
Tx/Rx operations according to 38.322 Rel.16
  Segmentation and reassembly procedures
  RLC Acknowledged mode supporting PDU retransmissions
  RLC Unacknowledged mode
  DRBs and SRBs establishment and handling
  Timers implementation
  Interfaces with PDCP, MAC
UE PDCP
Tx/Rx operations according to 38.323 Rel.16
  Integrity protection and ciphering procedures
  Sequence number management, SDU dicard and in-order delivery
  Radio bearer establishment/handling and association with PDCP entities
  Interfaces with RRC, RLC
UE RRC
Integration of RRC messages and procedures supporting UE 5G SA connection according to 38.331 Rel.16
  RRCSetupRequest/RRCSetup/RRCSetupComplete
  RRC Uplink/Downlink Information transfer carrying NAS messages transparently
  RRC Reconfiguration/Reconfiguration complete
  Support for master cell group configuration
Interface with PDCP: configuration, DCCH and CCCH message handling
Interface with RLC and MAC for configuration
UE NAS
Transfer of NAS messages between the AMF and the UE supporting the UE registration with the core network and the PDU session establishment according to 24.501 Rel.16
  Identity Request/Response
  Authentication Request/Response
  Security Mode Command/Complete
  Registration Request/Accept/Complete
  PDU Session Establishment Request/Accept
  NAS configuration and basic interfacing with RRC

## Slide 12: Functional splits in OAI 4G/5G
F1-C and F1-U
  Revised implementation under integration
  Interoperability testing with Acceleran ongoing
5G FAPI
  today all L1 procedures compliant with SCF 5G FAPI
  5G nFAPI
Fronthaul
  eCPRI (with AW2S)
  O-RAN 7.2 U-plane done (with Benetel)
  O-RAN 7.2 S/C-plane ongoing
  Interoperability with other RRUs (Mavenir, Foxconn) planned for beginning 2022
CU
RRH
O-RAN 7.2
eCPRI
3GPP F1
MAC/RLC
PHY
DU
SCF 5G FAPI
Notes: The status is the following:-F1-C (control plane) is enabled for 5G SA. This includes the exchange of the initial F1 setup messages between the CU and the DU, as well as their configuration updates; the transparent transfer of DL/UL RRC messages between the CU and the UE through the DU; the UE context management procedures exchanged between the CU and the DU; the establishment of GTP-U tunnels between the CU and DU, required for enabling user-plane traffic transfer over F1-U. These procedures allow to support the end-to-end UE attachment to the core network and the PDU Session establishment in CU/DU split deployment mode.-F1-U (User plane) is enabled for 5G SA. The new implementation of gtp-u has been updated to support user plane traffic over both N3 and F1-U interfaces concurrently. First IP traffic tests between the UE and the core network over F1-U have been successfully validated. Next steps will be to extend F1-C mainly with more UE context management procedures as per TS 38.473 Rel. 16, in the context of some planned interoperability tests between our DU and a commercial CU.
CI tests definded and to be set up
MR to be opened
Next: interoperability testing with AccelerRAN

## Slide 13: T1 LDPC Offload
Channel coding/decoding consumes most energy/processing time
  91% of total RX processing time in OAI
Xilinx T1 accelerator card
  Contains ZU19EG MPSoC and ZU21DR RFSoC
  Offload of forward error correction and fronthaul
  Bitstream and drivers provided by VVDN
LDPC channel decoding integrated in OAI
  Works with nr_ulsim and nr-softmodem
  Integration in develop ongoing
MAC/RLC
PHY
SCF 5G FAPI
FH
FEC
RRU
O-RAN 7.2 C/U/S
DPDK
BBDEV

## Slide 14: T1 LDPC Offload
NR-PUSCH, SCS 30kHz, 106PRB, 12OFDM symbols, 1 DRMS, SISO, TDL-C channel
Florian Kaltenberger, Hongzhi Wang, Saktivel Velumani, “Performance evaluation of offloading LDPC decoding to an FPGA in 5G baseband processing,” Workshop on Smart Antennas (WSA2021), Sophia-Antipolis, France, 10-12.11.2021.
execution time
See demo during second session

## Slide 15: L2 emulator for 4G and 5G NSA
Old L2 emulator replaced by more modular design
Based on 4G and 5G nFAPI
Channel proxy
NSA UE
Many bugfixes and performance improvements, especially for multiple UEs
Under integration in develop

## Slide 16: OAI4test project
Objectives
  develop an automatic protocol tester for UEs (4G and 5G) based on OAI
  compatible with TTCN tests defined by ETSI/3GPP
TTCN executable
eNB
PROXY
SYS port
SRB port
SQNS UE
TTCN logger
Sequans UE
logger
NFAPI interface
FAPI interface
IDL interface

## Slide 17: OAI4test project
Objectives
  develop an automatic protocol tester for UEs (4G and 5G) based on OAI
  compatible with TTCN tests defined by ETSI/3GPP
Achievements
  TTCN Sequans test framework (4G control plane), working in front of OAI eNB/proxy (L2 simulator) with Sequans 4G UE legacy simulator (3GPP certified)
  Able to run 3GPP 36523 6.1.2.2 (Cell selection / Qrxlevmin), TS 36.508 subclause 4.5.2.3 fully covered.
  Working on eNB configuration from TTCN (ASPs from 3GPP 36523-3 on TTCN EUTRA SYSTEM port)
  Starting to work on TTCN 5G test framework
Notes: Firecell is leading the enhancement of OAI to support TTCN test cases
  Introduce Virtual Time management on Proxy with Frame/SubFrame Acknowledge with UE. This enable the system to produce stable validation results
  Extend interface with UE in order to provision RSRP/RSRQ value to enable cell selection
  Implementation of system adapter APIs for SYS and SRB port.

## Slide 18: 5G non-terrestrial networks (Rel 17)

## Slide 19: 5G NTN roadmap

## Slide 20: Status of 5G NTN developments
Rel15 and Rel16 features necessary for NTN already part of public OAI repository
  FDD support
  Multiple DMRS support
  Phase Tracking Reference Symbols support
  10MHz bandwidth support
Initial development (5G GOA project)  to be merged Q2 2022 (after Rel 17 freeze)
  PHY Layer
    Consider timing relation for UL scheduling at gNB
    Extension of RAR window
    Extend OAI rf-simulator to support simulation of long delay
    Disable HARQ at gNB and UE
    Support for 5 MHz BW with 15 kHz SCS
    Testing/fixing OAI 5G NR SA with all the NTN features
  MAC Layer
    Uplink timing advance and RA procedure
    FDD Scheduling
    Multi-UE Support
    QoS scheduling
Next steps (5G LEO project)
  Xn Handover between transparent LEO satellites
  …

## Slide 22: 5G Core Project Group
https://openairinterface.org/oai-5g-core-network-project/
Sponsors Contributors

## Slide 23: OAI 5G CN – Current Status
23
Validation, CI/CD with
  Professional tester (dsTest, Developing Solutions):
    Testing AMF, SMF and UPF with simulated gNB/UE
    Bracket test for AMF, SMF (e.g., testing AMF with simulated SMF/UPF/gNB/UE)
  OAI gNB/OAI UE ( + Quectel/SIMcom modules)
  Commercial gNBs (Amarisoft/Baicell) /COTS UEs/Amarisoft UEs
  Open-source RAN simulators (gNBSim, UERANSIM)
OAI CN Progress Update Call
A solid and functional 5GC
  Basic procedures (with multiple UEs/multiple PDU sessions): connection and registration procedures, session management procedures
  Additional features: NF registration, NF discovery (e.g., to discover and select SMF, UPF), N2 handover, Paging, HTTP/2, FQDN support
Notes: 23

## Slide 24: OAI 5G CN – Current Status
24
Deployment, CI/CD
  Traditional/classic deployment on Servers/Virtual machines
  Automated deployment of NFs in Docker containers using Docker Compose
  Could-native deployment using Helm Chart on OpenShift cluster
OAI CN Progress Update Call
Two 5GC modes
  Minimal 5GC with AMF, SMF, NRF and UPF
  Basic 5GC with AMF, SMF, NRF, UPF, UDM, AUSF and UDR
Three UPF flavors:
  SPGW-U (from 4G) with additional features for 5G
  VPP-UPF (relying on VPP-Travelping, with DPDK support)
  Production grade UPF (Kaloom, on-going)
Notes: 24

## Slide 26: OAI 5G SA demo

## Slide 27: 5G NR Standalone Demo Setup

## Slide 28
Video comes here

## Slide 29: Thank You